## Slide 1: What is tcp ip protocol…?

## Slide 2: What is TCP…?
The Transmission Control Protocol (TCP) is a communications standard that enables application programs and computing devices to exchange messages over a network.
TCP is one of the basic standards that define the rules of the internet and is included within the standards defined by the Internet Engineering Task Force (IETF).
TCP organizes data so that it can be transmitted between a server and a client.
As a result, TCP is used to transmit data from high-level protocols that need all data to arrive.

## Slide 3: What is IP…?
The Internet Protocol (IP) is the method for sending data from one device to another across the internet.
IP is responsible for defining how applications and devices exchange packets of data with each other.
It is the principal communications protocol responsible for the formats and rules for exchanging data and messages between computers on a single network or several internet-connected networks.
IP is the main protocol within the internet layer of the TCP/IP.

## Slide 4: What is the Difference…?
TCP and IP are separate protocols that work together to ensure data is delivered to its intended destination within a network.
IP is the part that obtains the address to which data is sent.
TCP is responsible for data delivery once that IP address has been found.
The two protocols are frequently used together and rely on each other for data to have a destination and safely reach it, which is why the process is regularly referred to as TCP/IP.

## Slide 5: How Does TCP/IP Work…?
The TCP/IP model was developed by the United States Department of Defense to enable the accurate and correct transmission of data between devices.
TCP/IP divides communication tasks into layers that keep the process standardized, without hardware and software providers having to try and manage it themselves.
As a connection-oriented protocol, TCP establishes and maintains a connection between applications or devices until they finish exchanging data.
TCP/IP uses a three-way handshake to establish a connection between a device and a server, which ensures multiple TCP socket connections can be transferred in both directions concurrently.

## Slide 6: Four Layers of the TCP/IP Model
    Datalink layer
    Internet layer
    Transport layer
    Application layer
    UDP is an alternative to TCP that does not provide error correction, is less reliable, and has less overhead, which makes it ideal for streaming.